Attiny HV and ISP Programmer
Developed at TAMI
Tel-Aviv Makers International

---
Project goals
Main goal
  - High Voltage fuse reset of ATTami boards.
By products:
  - High Voltage fuse reset of Attiny components.
  - ISP programming of ATTami boards.
  - ISP programming of Attiny components.
  - ISP programming of various AVR based boards, under either 5V or 3.3V supply.
  - Acceptance test of ATTami boards.
  - Self contained ATTami bootloader loading (Not yet implemented)
ATTami HV and ISP Programmer
2/24/2015

---
Project structure
Arduino shield with the following features:
  - Charge pump circuit to provide the 11.5V for the HV programming.
  - Bi directional 5V to 3.3V level shifters.
  - Sockets to enable programming of ATTami boards and Attiny components.
  - Indicator LEDs.
  - ATTami ATP LEDs.
  - Control switches.

---
Charge pump circuit
Charge pump is a circuit that produces high voltage by switching of capacitors.
See: http://en.wikipedia.org/wiki/Charge_pump
In our case we produce 11.5V out of the Arduino 5V supply.
The 11.5V is controlled and regulated by the Arduino.

---
Bi directional 5V to 3.3V level shifters
4 MOSFET based bi-directional level shifters to shift the 5V Arduino I/O pins level to 3.3V.
See: http://delphys.net/d.holmes/hardware/levelshift.html

---
Sockets to enable programming of ATTami boards and Attiny components
  - Pogo-Pins socket to enable programming and testing of pinless ATTami boards.
  - Sockets to enable programming and testing of ATTami boards with upper or lower pins.
  - Socket for 8 pin ATtiny programming.
  - Socket for 14 pin ATtiny programming.
  - Socket for 6 pin ISP ribbon.
  - Socket for 10 pin ISP ribbon.

---
Control Switches
ISP – HV selector: Selects witch programming mode will be performed
3.3V – 5V selector: Selects the I/O pins level to conform with the external board connected to the ISP cables.
ISP Vcc – Target Vcc selector: Selects if The programmer will provide Vcc to the target board via the ISP cables.
ATTami test pushbutton: Provides Vcc to the ATTami board.
ATTami load bootloader: Initiate loading to the ATTami of the bootloader Hex file stored on the Arduino Flash memory. (This function is not yet implemented.)

---
Operation
There are two modes of operation, each of them runs under different environment:
  - HV fuse reset mode
  - ISP mode
There are two control buttons. (The control buttons functionality is the same under both modes of operation)
  - ATTami test button
  - ATTAMI load bootloader button

---
Operation cont.
HV fuse reset mode
  - In this mode you can:
    - Reset the fuses to factory default state.
    - Set the fuses to a predefined state.
    - Define the predefined fuses state.
  - To get into the mode:
    - Connect the Arduino to the PC via a USB cable
    - Set the ISP-HV selector to HV. (HB LED should on)
    - Load Arduino IDE
    - Open the Serial monitor (if necessary set it to 19200 baud rate)
  - To reset the fuses
    - Follow the instructions on the screen menu (While the HV is applied, in options 1 or 2, you should notice a short blink on the HV LED.)

---
Operation cont.
ISP programming mode
  - In this mode you can:
    - Upload a sketch into the ATtiny.
  - To get into the mode:
    - Connect the Arduino to the PC via a USB cable
    - Set the ISP-HV selector to ISB. (HB LED should pulse)
    - Load Arduino IDE
    - Set the board according to your ATtiny MCU
    - Set programmer to “Arduino as ISP
  - To program the ATtiny
    - Load your sketch into the IDE
    - Click on the “Upload” button. (error LED might blink at start and then turn off, pmode LED should blink while Uploading is performed and then turned off.)

---
Operation cont.
ATTami test
  - Operates on both HV and ISP modes.
  - On Both modes when not actually programming the ATtiny VCC is off and the reset pin is LOW.
  - When the test pushbutton is pressed Vcc is applied to the ATtiny and the reset pin goes HIGH. (The ATTami, or Attiny, will commence running)
  - Watch the test LEDs for the ATP pattern.

---
Operation cont.
ATTami load bootloader
  - Operates on both HV and ISP modes.
  - Operates even when the Arduino is not connected to a computer (5V source is nedded)
  - Momentary Push the “ATTami load bootloader” push buton.
  - The Arduino will upload the boot loader Hex file to the ATTami.
This function is not yet implemented

---
Software build
The software comprises 3 ino files that are on the same directory
The directory name is “HV_ISP_programmer”
The 3 files are: “HV_ISP_programmer.ino”, “ATTinyFuseReset.ino” and “ArduinoISP_ATTami”.
“HV_ISP_programmer.ino” contains the setup() and loop functions(), “ATTinyFuseReset.ino” contains the HV programming functions, “ArduinoISP_ATTami” contains the ISP functions.
The IDE compile and build them together and Upload the produced Hex file to the Arduino. You should do it once before using the Programmer.